## Slide 1
MOTOR
DRIVERS
BY - SUDHENSH

## Slide 2
CONTENT
01
02
03
04
05
06
WHAT?
WHY?
WORKING PRINCIPLE
L298N VS L293D
TYPES OF MOTOR DRIVERS
CONCLUSION

## Slide 3
Motors - High power
Control circuits - Low power
WHAT..?
As in the name, Motor drivers are used to control the working of motor(s). They act as an interface between motors and control circuits.

## Slide 4
WHY..?
To control
Motor
speed
To control direction
of rotation of
Motor
To reduce the
risk of controller burn outs and increase efficiency

## Slide 5
WORKING
PRINCIPLE
  Motor Drivers work on the concept of a switching circuit known as H-Bridge circuit.
  An H-bridge is used to drive a load, such as a DC motor, in both directions.

## Slide 6
S1 | S2 | O/P
0 | 0 | BREAK
1 | 0 | CLOCK
0 | 1 | ANTI-CLOCK
1 | 1 | BREAK
WORKING
S1
S2
S1b
S2b
+
-

## Slide 7
  Affordable
  40% - 70% efficiency
  used for DIY projects
  Ex. L298N
TYPES
BJT based
  Costlier
  91% - 95% efficiency
  used in bigger prototypes and products
  Ex. VNH2SP30
MOSFET based

## Slide 8
Lorem ipsum dolor sit amet, consectetur adipiscing elit. Duis vulputate nulla at ante rhoncus, vel efficitur felis condimentum. Proin odio odio.
L298N VS L293D
  L298N 2A based Motor driver
  MOTOR VOLTAGE = 5V - 46V
  MOTOR CURRENT = 2A (cont.)
  LOGIC VOLTAGE = 5V
  2 motors or 1 stepper motor
  WEIGHT = 26g
  IMBUILT HEAT SINK
  COST = AROUND 110 Rs.
  Arduino L293D Motor driver shield
  MOTOR VOLTAGE = 4.5v - 36V
  MOTOR CURRENT = 600mA(cont.)
  LOGIC VOLTAGE = 5V
  4 motors or 2 stepper motors
  WEIGHT = 20g
  NO HEAT SINK
  COST = AROUND 85 Rs.

## Slide 9
Hence I conclude that Motor drivers play and important role in Robotics as they help in controlling one or more motors without any physical human intervention and also reduce the risk of control circuit burnouts.
CONCLUSION